Section 08 3497

FIXED fabric Draft curtain

# General

## Summary

### Section Includes:

#### Lightweight fixed fabric, semi-permanent or temporary, fire barrier system for large vertical openings.

### Related Requirements:

#### 09 9100 - Paint: Field painting of specified components.

## SUSTAINABLE DESIGN REQUIREMENTS

### LEED-NC: Comply with Section 01 8100 Sustainable Design Requirements including, without limitation, submittal and documentation requirements.

### Credit/Point Goals Applicable To This Section: In addition to global Project credit/point goals:

#### Materials & Resources - Construction Waste Management

#### Materials & Resources - Recycled Content

#### Materials & Resources - Regional Materials

#### Indoor Environmental Quality - Construction IAQ Management Plan

## submittals

### Comply with Section 01 3300(Submittal Procedures:

#### Product Data

#### Shop Drawings:

##### Include opening dimensions.

##### Show and identify related work performed under other sections of the specifications

#### Quality Assurance/Control Submittals:

##### Certifications

##### Manufacturer’s installation instructions and testing procedures

## closeout submittals

### Comply with Section 01 7700(Project Closeout:

#### Manufacturer’s Warranty

## Quality Assurance

### Pre-Installation Meeting:

#### Schedule and convene a pre-installation meeting prior to commencement of field operations with representatives of the following in attendance: Owner, Architect, General Contractor, and fire barrier system sub-contractor.

#### Review substrate conditions, requirements of related work, installation instructions, storage and handling procedures, and protection measures.

#### Document responsibilities of various parties and deviations from specifications and installation instructions.

## Delivery, Storage, and Handling

### Comply with Section 01 6600(Delivery, Storage, and Handling.

### Comply with manufacturer’s instructions.

## Warranty

### Provide manufacturer’s standard one year warranty

# Products

## ManufactureD units

### SG Draft

### Manufacturer:

#### Smoke Guard, 287 Maple Grove, Boise, Idaho 83704, www.smokeguard.com

## Performance / DESIGN CRITERIA

### Maximum Opening Sizes (feet):

#### Unlimited

## Components

### Curtain Fabric:

#### SG Tex 10

#### Glass filament fabrics of glass fiber material coated on both sides.

#### ASTM E136 Certified

#### ASTM E84 Certified

### Side Assembly:

#### Manufacturer’s standard

### Bottom Bar:

#### Manufacturer’s standard type

## fabrication

### Installation Configuration:  Attached directly to opening perimeter.

### Fabricate and install mounting brackets, hardware, and fasteners needed to attach curtain assembly to substrate.

# Execution

## Examination

### Examine substrates upon which work will be installed.

#### Verify related work performed under other sections is complete and in accordance with Shop Drawings.

#### Verify wall surfaces are acceptable for installation of fire barrier system components.

### Coordinate with responsible entity to perform corrective work on unsatisfactory substrates.

### Commencement of work by installer is acceptance of substrate.

## INSTALLATION

### Install fire barrier system components in accordance with manufacturer’s installation instructions.

End of Section